## Slide 1
TITLE PAGE
SMART INDIA HACKATHON 2026
Problem Statement ID
SIH26177
Problem Statement Title
<paste exact title from the SIH portal> - autonomous UAV-based search, detection and assistance for disaster survivors
Theme
Robotics & Drones
PS Category
Hardware
Organization
Qualcomm Inc.
Team ID
<TEAM ID>
Team Name (registered on portal)
<TEAM NAME (as registered on portal)>
Institute (AISHE)
<INSTITUTE NAME> · <AISHE CODE>
Notes: Idea submission, slide 1 of 6. Nothing to say here beyond the portal-exact problem statement title - judges check it matches.

## Slide 2
IDEA TITLE
@SIH Idea submission - Template
<TEAM NAME (as registered on portal)>
2
SAHYOG - the phone-powered thermal search drone
IDEA / SOLUTION:
▸ The problem, in our words: in floods and quakes, survivors are lost in the first hour because search is a human watching thermal video; GPS, networks and roads fail together; and at survey altitude a human body is 4-10 pixels - smaller than one grid cell of an off-the-shelf detector (measured mAP50 0.0009, i.e. blind). Affected: flood/quake survivors and the SDRF/NDRF/district teams who reach them late.
▸ The solution, in our words: an autonomous drone that fuses a radiometric LWIR camera with an Android phone's RGB camera, detects survivors with a YOLO11n carrying an added stride-4 (P2) head, passes every detection through physics gates, and returns 200-byte verified survivor packets over LoRa - entirely on-device, no internet at any step.
▸ The unfair advantage: the phone supplies six subsystems (stabilised RGB, INT8 NPU, VIO, 4G relay, display, backup battery) = Rs 0 of a Rs 35,000+ payload; its Hexagon DSP is the same family as this PS's target QCS6490 board - one model, two destinations.
▸ Who it serves: district disaster control rooms; first-hour search of 9 ha per 10-minute pass, night, smoke or canopy.
Notes: Problem first, then solution, then the advantage, then the beneficiary - in that order, one breath each. The 4-10 pixel number is the hook: it is why every other approach fails and why ours is shaped the way it is.

## Slide 3
TECHNICAL APPROACH
@SIH Idea submission - Template
<TEAM NAME (as registered on portal)>
3
▸ Detection: YOLO11n + bundled P2 (stride-4) head - the single largest accuracy change for sub-8 px targets (0.0009 -> 0.234 mAP50, 260x); thermal trained with radiometric augmentation; ONNX opset 12 -> INT8 w8a8 QNN for Hexagon behind a >=97% recall-retention gate.
▸ Physics gates (the trust layer): radiometric test (body 30-37 C vs flood water 15 C; sun-heated roofs rejected), projected-extent geometry veto, two-pass confirmation (find at 45 m, confirm at 22 m), Platt-scaled confidences so the belief map composes probabilities.
▸ Search strategy: lawnmower lanes with spacing = sensor swath x detection-probability target (search theory); every negative observation lowers the belief map and drives re-visit.
▸ Navigation: EKF source-manager; phone VIO + lidar when GNSS is denied; position sigma monitored, sortie ends past 25 m.
▸ Communications: LoRa 900 MHz store-and-forward, 200-byte acked packets; ELRS is control-only so the alert path never depends on it.
▸ Safety: 12-rule supervisor (25% reserve, geofence, wind, telemetry silence) outranks the mission.
▸ Stack: Python - ArduPilot/MAVLink - ONNX Runtime + QNN - ultralytics fine-tune on a free Kaggle T4 - datasets HIT-UAV / AIResQ / SARD.
Notes: Seven method lines, each ending in a number or a named algorithm. If a judge interrupts, any line can be defended from the repository. Do not read this slide; point at it.

## Slide 4
FEASIBILITY AND VIABILITY
@SIH Idea submission - Template
<TEAM NAME (as registered on portal)>
4
▸ Technical: 180+ automated tests pass; end-to-end simulated sorties today; phone bridge benchmarked on real hardware (15.0 fps RGB, 29.6 Hz VIO, 69 ms worst gap); ONNX + INT8 artefacts on disk; onboard budget 165 ms vs 500 ms available; every layer has a fallback.
▸ Financial: phone replaces Rs 35,000+ of bought subsystems; airframe ~Rs 40k; radiometric LWIR ~Rs 15-25k -> under Rs 1 L per aircraft vs Rs 3 L+ conventional; zero cloud cost, all inference on-device.
▸ Market: every district control room already owns the compute (phones); no new supply chain for the AI.
▸ Operational: one-operator launch; crew training is one Android app; maintenance is Android updates.
POTENTIAL CHALLENGES AND RISKS -> STRATEGIES FOR OVERCOMING
▸ LWIR lead time -> Boson 320 second source.
▸ Small-target recall gap -> P2 head + 640x512 real-data fine-tune, already running on the free-GPU path.
▸ INT8 accuracy loss -> w8a16 fallback behind the same >=97% gate.
▸ Monsoon window -> dry-season trials in Bihar.
▸ No local GPU -> documented free-tier GPU runbook.
Notes: Four feasibility axes in the template's own order, then the risk table. Naming risks with owned mitigations is the single cheapest credibility win in this round.

## Slide 5
IMPACT AND BENEFITS
@SIH Idea submission - Template
<TEAM NAME (as registered on portal)>
5
POTENTIAL IMPACT ON THE TARGET AUDIENCE
▸ Positive: first-hour coverage at machine speed (9 ha per 10-minute pass); measured precision 1.000 - zero false alarms, so ground teams stop climbing wrong rooftops; LWIR works at night, through smoke, under canopy; verified reports survive total network loss.
▸ Negative, named and mitigated: technology-adoption risk -> phone-first design, one app, heuristic fallback so a missing model never grounds the aircraft; LWIR cost -> offset by the phone's Rs 35k substitution.
BENEFITS OF THE SOLUTION
▸ Social: golden-hour rescues reached in the golden hour; rescuers routed around hazards (A* over the flood field); equity - district-affordable, not metro-affordable.
▸ Economic: Rs 0 compute payload; one airframe re-tasked across flood, wildfire, landslide and coastal SAR by swapping modality weights, not mission code.
▸ Environmental: electric airframe replaces helicopter search hours; minimal noise over distressed communities.
Notes: Answering the template's 'negative impact' prompt is the differentiator: ninety percent of teams pretend there are none. We name two and close both.

## Slide 6
RESEARCH AND REFERENCES
@SIH Idea submission - Template
<TEAM NAME (as registered on portal)>
6
▸ Datasets studied: HIT-UAV (2,898 aerial LWIR frames) - AIResQ (airborne thermal SAR; source of the honest mAP50 ~ 0.55 ceiling) - SARD (1,981 SAR postures) - VisDrone - HERIDAL - RescueNet.
▸ Literature: MDPI J. Imaging 11(12):436 - 75k-image aerial-thermal benchmark: RT-DETR-L 5.0% vs YOLO 10.7-11.6% AP on small objects (why we fly a CNN, not a transformer) - Ultralytics YOLO11 benchmarks - Koopman search theory - Platt (1999) probability calibration.
▸ Existing solutions and our difference: commercial thermal drones = human-watched video, no autonomy, no rejection of false alarms; research UAV SAR = RGB-only or cloud-dependent; ours = on-device radiometric detection + physics gates + phone-borne compute, every claim traceable to a checksummed artefact in our repository.
TEAM
<Member 1> AI/perception · <Member 2> flight & safety · <Member 3> comms & GCS
<Member 4> mobile bridge · <Member 5> airframe & power · <Member 6> data & field ops
Contact: <email> · Thank you - live demo available.
Notes: Close on the difference line, then offer the demo. 'Every claim on these six slides traces to a checksummed artefact in our repository - we would rather show you the measurement than ask you to trust the adjective.'